## Slide 1
Next Generation GOES Spacecraft Design to Improve Quality of NOAA Weather Data
Loren Slafer, Charles Rubin
The Boeing Company
For the next generation GOES satellite, Boeing Satellite Systems developed a unique spacecraft bus design that will substantially improve the quality of NOAA’s GOES weather data
This new GOES N-P design enables the precision spacecraft performance that will be required for GOES high-resolution instruments
The key features of this design concept includes
  Stellar inertial attitude determination (SIAD) control system
  Imager and Sounder collocated with the star trackers on a common base plate supported by structural flexures and attached to the nadir panel
  A single panel solar array provides a clear field of view (FOV) for the Imager and Sounder coolers, maximizing their radiometric performance
System design includes
  Enhanced Kalman filter design to meet 10 microradian bus pointing
System validation using high-fidelity simulator including
  On-board computer and flight software
  Star Tracker
  Model of real-time on-orbit operations
The BSS design for the next-generations of GOES focused on
‘Flying the instruments’
GOES weather data will benefit from SIAD control system, enabling the National Weather Service to improve its ability to protect the life and property of the nation’s citizens